#### Dividing perennials

Most perennials benefit from division every two to three or so years to maintain health and vigour, as well as to propagate new plants.

#### Timing

Plants can be divided successfully at almost any time if kept well-watered afterwards. However, division is usually most successful while plants aren’t in active growth. Divide summer-flowering plants in spring or autumn, and spring-flowering plants in summer after flowering.

#### Soil preparation

Work bulky organic matter, such as garden compost or well-rotted manure, into the planting hole. If re-planting into the same site then also add a slow-release fertiliser such as bonemeal.

#### Lifting and dividing plants

Some plants, such as Ajuga (bugle) produce individual plantlets which can simply be teased out and re-planted. Most however require lifting and dividing.

Lift plants gently with a garden fork, working away from the crown centre to limit root damage. Wash off excess soil so that roots are clearly visible.

Small, fibrous-rooted plants such as Heuchera or Epimedium (see left) can be pulled apart. Larger fibrous-rooted perennials such as Hemerocallis require two garden forks inserted into the crown back-to-back (see above). Lever the forks to loosen the root mass.

Plants with woody crowns (e.g. Helleborus) or fleshy roots (e.g. Delphinium) require cutting with a spade or knife. Aim to produce clumps containing three to five shoots.

#### Aftercare

Plant divisions as soon as possible and water them in well. Alternatively pot up individually to build up size, overwintering pots in a frost-free environment.

#### Further information